Instructions To Bidders

The Clay County Indiana Board of Commissioners are requesting Bids to relocate and enhance the radio communications systems from the old Clay County jail to the new facility at 611 Jackson Street, Brazil, IN 47834.  Bids are to be received at Clay County Auditor’s Office, 609 E. National Avenue, Brazil, IN  47834.

The scope of this project is to supply and install 3 CRT based radio dispatch work stations, new radio base stations, associated antennae systems, grounding and relocate the existing 120 ft. tower.

The Clay County Indiana Board of Commissioners reserves the right to accept or reject any bid on a section by section basis. The Board also reserves the right to accept or reject any Bid or all Bids in whole or in part and to waive any formal defects or technicalities when deemed in the best interest of Clay County.

In order for each Bidder to be deemed responsive, they must clearly note, with reference to the relevant item, any and all deviations to these specifications. Such notations shall state the reason for the deviation and why the proposed deviation is superior to or equal to the system or method specified. Failure to provide this information will be just cause for the proposal to be rejected as non-responsive.

The successful bidder must install all equipment in accordance with all applicable code and manufacturer recommendations. Special emphasis will be given to documentation and detailed labeling of cables, terminations, etc. Upon completion, a complete set of Owners Manuals and a detailed Site Map must be presented to the Clay County Board of Commissioners.

The Clay County Board of Commissioners, while composing these Bid Specifications has strived to be complete and accurate, making no warranty to the fact.

Scope of Work

Section I	Radio Dispatch Consoles

The successful bidder shall supply and install a Zetron model 4000 CRT based radio dispatch system. This system is to consist of 3 dispatch work stations with 19”LCD displays, model 4217B audio panels and Integrator RD software.

Each work station is to be complete with desk top turrent, track ball, gooseneck microphones, foot switch, head set jack box and paging options to facilitate a complete system.

The common controller card cage shall be the Zetron model 4020. The Model 4020 shall be configured with the following:

- Redundant power supplies

- Radio control cards for a minimum of 14 channels

- 8 cross patches

- Intelligent radio interface modules to facilitate communications with contractor supplied radio to interface with the State of Indiana Project Hoosier Safe-T.

- One auxiliary IO card

- Spare boards, modules, parts etc, as recommended by the manufacturer.

- All cables, punch blocks, arrestor and documentation to make a complete system.

The contractor shall supply a X-Mark Equipment cabinet with locking tempered glass doors, cooling fan and power strip. This cabinet is to hold the above common controller equipment.

Section II	Radio Base Stations

The contractor shall supply and install the following equipment:

6  	VHF 50 watt VHF rack mount base station Kenwood Model TK-750

or equivalent. The base stations shall be complete with proper tone remote

termination panel and rack mount power supply to make a complete unit.

The above stations to be configured to communicate on the following networks:

- Clay County Sheriff

- Clay County Fire

- Point to Point

- Clay County Ambulance

- Brazil Police Department

- Brazil Fire Department

- 800 MHz base station to communicate to the Hoosier Safe-T network.

This base is to directly interface to the Zetron system and allow unit identifications to be displayed and group changes at each dispatch work station.

- VHF transmitter and receiver antenna combining systems.  This antenna

multi-coupling system is to combine all VHF frequencies at this site into 3 antennas. This system shall be TX/RX Systems Model 74-37-05240-E or equivalent.

*See attached drawing

The contractor shall relocate and install the following R.F. equipment from the old jail to the new location:

1	MA/COM Auxiliary receiver cabinet

1	E.F. Johnson Ambulance repeater

The contractor shall provide all coax connectors, cables, arrestors, entrance panel with boots, cabinets, cable tray, grounding, etc, to make a complete system.

Section III	Relocate Existing Tower

The contractor shall provide all services necessary to relocate the existing 120 ft tower with antennas and feed lines to the new foundation that has been installed by others. The new foundation is located on the south west corner of the new jail.

The contractor shall be required to install and supply a halo ground system with cad weld connections.

The contractor shall supply the 18 port entrance panel that will be installed by others.

Section IV  Warranty/Maintenance

Successful bidder shall provide a minimum warranty for all equipment and shall be responsible to repair or replace all broken or unusable pieces of equipment.  Successful bidder must also provide minimum response time of no later than 1 hour.